SpaceCobot Operation Steps

Check all the connections:
 1) Motor ESCs connected to pixhawk with signal on the bottom pin.
 2) Power cable to raspberry pi connected to 2nd GPIO pin of the second row.
 3) Raspi not connected to any other power source
 4) Reciever connected
 5) Arming switch connected
 6) Micro USB cable from pixawk to raspi
7) Goggles on your face and gloves on your hand

Propeller mounted securely to the motors

Switch on the wifi.

Plug in the battery. IF arming switch is already armed (flickering in tones of two) DISARM IT.

Switch on the transmitter pressing the binding switch so as to bind it with the reciever. Keep the transmitter within your arms' reach.

SSH into raspberry pi. Open at least four terminals.

Start MAROS: - $ roslaunch mavros px4.launch
Start Nodes:- $ rosrun scobotros_alg scobotros_alg
(run the first executable)

In a separate terminal check the rostopic : rostopic echo /important_values. This will print out all the important values required.
Check all the values expecially these:
1) Desired RPY
2) Desired Position
3) Attitude PIDs
4) Position PIDs
5) Intial RPMs
6) Desired angular velocity
7) Flight_Mode
Record ROSBAG
Record on Camera

Hold the Space Cobot and ARM the pixhawk. MOTORS SHOULD START MOVING.

Follow the task requirements prepared beforehand.